## Slide 1
Series Circuit Analysis

## Slide 2
There are three form of Ohm’s Law :
Where :
I = Current
V= Voltage
R= Resistance
Ohm’s Law Formula

## Slide 3
I= V/R
12/3 = 4
10/3= 3.3 A
8/3= 2.6 A
6/3= 2 A
4/3= 1.33 A
2/3= 0.6 A

## Slide 5
V = ?
R1
2.0 Ω
Calculate the voltage if the current is 0.5 A and the resistance is 2.0 Ohms.
I = 0.5
R= 2.0 ohms
V= I*R 0.5*2.0 = 1 Volt
Problem 1

## Slide 7
V = 1.2
R1
0.6 Ω
Calculate the Current if the voltage is 1.2 V and resistance is 0.6 Ω
V= 1.2
R= 0.6 ohms
I = 1.2/0.6 = 2 A
Problem 2

## Slide 9
V 2.2
R1
?
Calculate the resistance if the current is 1.1. and the voltage is 2.2 volt.
V= 2.2
I = 1.1
R= 2.2/1.1 = 2 ohms
Problem 3

## Slide 11
7 Ω
5 Ω
4 Ω
6 Ω
Solve for the resistance , R when V and I are given
V= 14V , I= 2A R= ?
V= 25V , I= 5A R= ?
V= 6V , I= 1.5A R= ?
V= 24V , I= 4A R= ?
Problem 4

## Slide 12
12V
R1
3 Ω
R2
3 Ω
R3
3 Ω
Find the Total Voltage as VT and Total Current IT
Total voltage = 12 V
Total Resistance= 9 Ω
Total Current = V/I 12/9 = 1.3 A
Problem 5

## Slide 13
120 V
R1
15 Ω
R2
5 Ω
R3
20 Ω
Find the following in given circuit.
V1 = 45V
V2 = 15 V
V3 = 60 V
VT = 120 V
I1
I2
I3
IT
R1
R2
R3
RT
V1
V2
V3
VT
R1= 15 Ω
R2 = 5 Ω
R3 = 20 Ω
RT = 40 Ω
I1 = 3 A
I2 = 3 A
I3 = 3 A
IT = 3 A

## Slide 14
60 V
R1
17 Ω
R2
12 Ω
R3
11 Ω
Find the following in given circuit.
V1 = 25.5V
V2 = 18 V
V3 = 16.5 V
VT = 60 V
I1
I2
I3
IT
R1
R2
R3
RT
V1
V2
V3
VT
R1= 17 Ω
R2 = 12 Ω
R3 = 11 Ω
RT = 40 Ω
I1 = 1.5 A
I2 = 1.5 A
I3 = 1.5 A
IT = 1.5 A