## Slide 1: STP and RSTP in Networking
Spanning Tree Protocol & Rapid Spanning Tree Protocol
With Real-Life Examples
By Javed, M.Shayan, Tushal and Uzair

## Slide 2: Introduction
• In Ethernet networks with multiple switches, loops can occur.
• Loops cause broadcast storms, duplicate frames, and network failure.
• STP (Spanning Tree Protocol) and RSTP (Rapid STP) are used to prevent loops.
• They ensure a loop-free, efficient, and reliable network.

## Slide 3: What is STP (Spanning Tree Protocol)?
STP is a network protocol used in switches.
Its job is to stop loops when many switches are interconnected.
It does this by blocking extra links and keeping only one safe path for data.
If the main path fails, it can unblock another path to keep the network running.
Protocol: set of rules

## Slide 4: What is RSTP (Rapid Spanning Tree Protocol)?
RSTP is an improved / Advanced version of STP.
RSTP introduced new port roles (such as Alternate Port and Backup Port).
It also stops loops in a network of switches.
The difference is → RSTP is much faster than STP.
If a link fails, RSTP finds a new path in just 1–10 seconds (STP takes 30–50 seconds).

## Slide 5: Differences Between STP and RSTP
Feature | STP | RSTP
IEEE Standard | 802.1D | 802.1w
Convergence Time | 30-50 | 1-10
Port Stages | Disabled, Blocking, Learning, Listening and Forwarding | Discarding Learning Forwarding
Recovery Speed | Slow recovery from link layer | Faster recovery from link layer

## Slide 6: Real-Life Example: Company Network
• A company connects its offices with multiple switches.
• Redundant links are added for backup.
• Without STP/RSTP → loops occur, causing network storms.
• With STP → redundant links are blocked, network is stable but slow to recover.
• With RSTP → network recovers within seconds after link failure.

## Slide 7: Real-Life Example: Traffic Analogy
Imagine a city with many roundabouts (loops).
If cars keep going in circles → there will be a traffic jam (like data looping in a network).
STP = traffic police who closes one road so cars move in a clear path.
RSTP = smart traffic lights that quickly open another road if one road is blocked.

## Slide 8: Conclusion
• STP and RSTP are useful protocols for loop-free switching networks (to prevent loop-structure).
• STP ensures stability in the network but is slow in recovery.
• RSTP improves recover our network rapidly, Hence it’s the advanced version.
• Real-life: Like traffic management systems preventing road congestion.
• Modern networks prefer RSTP for efficiency and speed.