## Slide 1: Digital Logic Design Introductory Concepts Fall-2025
Instructor: Muhammad Ismail Qureshi
Computer Science Department
Sukkur IBA University
Kandhkot Campus

## Slide 2: OUTLINE

## Slide 3: Key Terms

## Slide 4: Objectives

## Slide 5: Introduction of the Course

## Slide 6: Before Diving into the DLD exploring Electron and Electronics
Electronics is a branch of physics and engineering
deals with the study and application of electron behavior, flow, and control
particularly in circuits and devices that manipulate electrical currents
encompasses the design, construction, and operation of devices that use electricity to control, communicate, and process information.
Electronics focuses on the movement of electrons
  how they can be harnessed to perform specific tasks
    such as powering devices, transmitting signals, or processing information.

## Slide 7: Before Diving into the DLD exploring Electronics
Key Components
  transistors, diodes, and integrated circuits
    to control and amplify electrical currents.
Applications
  computers, smartphones, televisions, and countless other devices that shape our daily lives.
Relationship to Physics and Engineering
  Electronics is a subfield of physics, specifically focusing on the behavior of electrons, and also a field of electrical engineering, which applies these principles to design and build electronic systems and devices.

## Slide 8: Before Diving into the DLD exploring Electronics
a branch of Physics that deals with the theory and use of devices in which the electrons travel through a vacuum, gas, or a semiconductor medium
the branch of science and technology ,which deals with the electrical circuits and equipment like diodes, transistors and relays
the study of how to control flow of electrons
electronic components include diodes, transistors, and integrated circuits

## Slide 9: Analog Vs Digital

## Slide 10: Analog Quantities Electronic circuits can be divided into two broad categories, digital and analog.
analog electronics involves quantities with continuous values.
interfacing between analog and digital is important
An analog* quantity is one having continuous values
Most things that can be measured quantitatively occur in nature in analog form.
air temperature, time, pressure, distance, and sound, all the infinite values in between
continuous variables that can take on any value within a given range
Analog quantities change smoothly and continuously
There are no sudden jumps or gaps in the values
data is transferred in a wave
analog computer are oscilloscope, television, autopilot, telephone lines, speedometer

## Slide 11: Analog Quantities

## Slide 12: Digital Quantities
Digital electronics involves quantities with discrete values
A digital quantity is one having a discrete set of values
Rather than graphing the temperature on a continuous basis
you just take a temperature reading every hour
Now you have sampled values representing the temperature at discrete points in time (every hour) over a 24-hour period, as indicated in Figure 1–2.
effectively converted an analog quantity to a form that can now be digitized by representing each sampled value by a digital code
set of defined states
often using binary code (0s and 1s) to represent information
Key Characteristics of Digital Quantities:
  Discrete Values:
    limited set of specific, separate values

## Slide 13: Digital Quantities
  Binary Representation:
    Digital systems commonly use binary code (0 and 1) to represent these discrete values.
  Easier Processing and Storage:
    easier to process, store, and transmit due to its discrete nature and the ability to use digital circuits.
  Reduced Noise and Distortion:
    Digital signals are less affected by noise and distortion compared to analog signals, leading to more reliable information transfer.
  Examples of Digital Quantities:
    Digital clocks: Show time using discrete numbers (e.g., 10:30 AM).
    Digital music: Audio is stored as a series of discrete values representing the sound wave.
    Digital cameras: Capture images using a grid of discrete pixels.
    Computers and calculators: Process information using binary code.
    Switches (on/off): Representing two distinct states.
    Counters: Counting discrete items or events.
    Pulse-width modulation (PWM): Used in various applications to control power and other parameters.

## Slide 14: Digital Quantities
  less noise, distortion, and interference
  Digital circuits can be reproduced easily in mass quantities at comparatively low costs
  Digital signal processing is more flexible because DSP operations can be altered using digitally programmable systems
  Computers:
    Digital signals are fundamental to how computers process and store information. Every keystroke on a keyboard, every mouse click, and every operation within the CPU relies on digital signals.
  Digital Communication:
    The internet, smartphones, and other digital communication systems use digital signals to transmit data, voice, and video.
  Consumer Electronics:
    Digital signals are used in devices like smartphones, digital cameras, smart TVs, MP3 players, and more, enabling them to process and display information accurately.

## Slide 15: Digital Quantities
  Control Systems:
    In industrial automation, digital signals are used to control various processes and devices, such as in programmable logic controllers (PLCs).
  Audio and Video:
    Digital audio (like MP3s) and digital video (like MP4s) are common examples of how digital signals are used to represent and transmit media.
  Microcontrollers and Processors:
    Digital signals are used extensively in the communication and processing within microcontrollers and processors in various electronic devices.
  In essence, digital signals are the foundation of modern technology, enabling the accurate and efficient processing and transmission of information in a wide range of applications.

## Slide 16: Digital Quantities
  Disadvantage of Digital Signals
    Develop quantization and round-off errors
    Systems and processing is more complex
    A higher bandwidth is required for data communication in comparison to analog transmission of an equivalent information
    Digital systems and processing are typically more complex.
    digital data can be processed and transmitted more efficiently and reliably than analog data.
    great advantage when storage is necessary
    music when converted to digital form can be stored more compactly and reproduced
    with greater accuracy and clarity than is possible when it is in analog form.
    Noise (unwanted
    voltage fluctuations) does not affect digital data nearly as much as it does analog signals.

## Slide 17: Digital Quantities

## Slide 18: An Analog System
A public address system, used to amplify sound so that it can be heard by a large audience, is one simple example of an application of analog electronics.

## Slide 19: A System Using Digital and Analog Methods

## Slide 20: Mechatronics
Both digital and analog electronics are used in the control of various mechanical systems.
The interdisciplinary field that comprises both mechanical and electronic components is known as mechatronics.
Mechatronic systems are found in homes, industry, and transportation.
Most home appliances consist of both mechanical and electronic components.
Electronics controls the operation of a washing machine in terms of water flow, temperature, and type of cycle.
Manufacturing industries rely heavily on mechatronics for process control and assembly.

## Slide 21: Mechatronics
In automotive and other types of manufacturing, robotic arms perform precision welding, painting, and other functions on the assembly line.
Automobiles themselves are mechatronic machines
a digital computer controls functions such as braking, engine parameters, fuel flow, safety features, and monitoring.

## Slide 22: Mechatronics

## Slide 23: Assignment #1

## Slide 24: 1–2 Binary Digits, Logic Levels, and Digital Waveforms

## Slide 25: Digital electronics
circuits and systems
  two possible states.
    represented by two different voltage levels
      A HIGH and a LOW
The two states can also be represented by current levels, bits and bumps on a CD or DVD, etc.
In digital systems such as computers
  combinations of the two states
    called codes
      Are used to represent numbers, symbols, alphabetic characters, and other types of information.

## Slide 26: Digital electronics
The two-state number system is called binary
  its two digits are 0 and 1
    A binary digit is called a bit.

## Slide 27: Binary Digits
Each of the two digits in the binary system, 1 and 0, is called a bit
which is a contraction of the words binary digit (b_it)
Generally, 1 is represented by the higher voltage, which we will refer to as a HIGH
0
  lower voltage level
    positive logic
Negative logic is reverse
  Another system in which a 1 is represented by a LOW and a 0 is represented by a HIGH is called negative logic.
Groups of bits (combinations of 1s and 0s), called codes
  used to represent numbers, letters, symbols, instructions, and anything else required in a given application.

## Slide 28: Logic Levels
The voltages used to represent a 1 and a 0 are called logic levels.
a HIGH can be any voltage between a specified minimum value and a specified maximum value.
Likewise, a LOW can be any voltage between a specified minimum and a specified maximum.
There can be no overlap between the accepted range of HIGH levels and the accepted range of LOW levels.
the HIGH input values for a certain type of digital circuit technology called CMOS may range from 2 V to 3.3 V and
the LOW input values may range from 0 V to 0.8 V.
If a voltage of 2.5 V is applied, the circuit will accept it as a HIGH or binary 1.
a voltage of 0.5 V
  accept it as a LOW or binary 0

## Slide 29: Logic Levels

## Slide 30: Digital Waveforms
Digital waveforms consist of voltage levels that are changing back and forth between the HIGH and LOW levels or states
positive-going pulse
  normally LOW level to its HIGH level and then back to its LOW level
negative-going pulse
  in Figure 1–7(b) is generated when the voltage goes from its normally HIGH level to its LOW level and back to its HIGH level.
A digital waveform is made up of a series of pulses.

## Slide 31: Digital Waveforms

## Slide 32: The Pulse
a pulse has two edges
  a leading edge that occurs first at time t0
  a trailing edge that occurs last at time t1
For a positive-going pulse
  the leading edgeis a rising edge
  the trailing edge is a falling edge

## Slide 33: nonideal pulse

## Slide 34: nonideal pulse
The overshoot and ringing
  sometimes produced by stray inductive and capacitive effects.
The droop
  caused by stray capacitive and circuit resistance
    Forming an RC circuit with a low time constant

## Slide 35: nonideal pulse

## Slide 36: Waveform Characteristics
series of pulses, sometimes called pulse trains
  classified as either periodic or nonperiodic
a fixed interval, called a period (T)
frequency ( f ) is the rate at which it repeats itself and is measured in hertz (Hz).
The frequency ( f ) of a pulse (digital) waveform is the reciprocal of the period.

## Slide 37: Waveform Characteristics
An important characteristic of a periodic digital waveform is its duty cycle
  ratio of the pulse width (tW) to the period (T )

## Slide 38: Waveform Characteristics

## Slide 39: Waveform Characteristics

## Slide 40: Numerical

## Slide 41: A Digital Waveform Carries Binary Information
Binary information
  handled by digital systems
    appears as waveforms
      that represent sequences of bits
  When the waveform is HIGH,
    a binary 1 is present
  when the waveform is LOW,
    a binary 0 is present
  Each bit in a sequence occupies a defined time interval
    Called a bit time.

## Slide 42: A Digital Waveform Carries Binary Information
The Clock
  In digital systems
    all waveforms are synchronized with a basic
      timing waveform called
        the clock.
  The clock is a periodic waveform
    in which each interval between pulses (the period)
      equals the time for one bit.
    Figure 1–11. Notice that, in this case, each change in level of waveform A occurs at the leading edge of the clock waveform.
    During each bit time of the clock, waveform A is either HIGH or LOW.
    These HIGHs and LOWs represent a sequence of bits as indicated.
    The clock waveform itself does not carry information.

## Slide 43: A Digital Waveform Carries Binary Information
The Clock

## Slide 44: A Digital Waveform Carries Binary Information
Timing Diagrams
  A timing diagram
    is a graph of digital waveforms showing the actual time relationship of two or more waveforms and how each waveform changes in relation to the others.
    can determine the states (HIGH or LOW) of all the waveforms at any specified point in time and the exact time that a waveform changes state relative to the other waveforms
  Figure 1–12 is an example of a timing diagram made up of four waveforms.
    the three waveforms A, B, and C are HIGH only during bit time 7 (shaded area) and they all change back LOW at the end of bit time 7.

## Slide 45: A Digital Waveform Carries Binary Information
Timing Diagrams

## Slide 46: A Digital Waveform Carries Binary Information
Data Transfer
  Data
    refers to groups of bits that convey some type of information.
  Binary data
    represented by digital waveforms
    ransferred from one device to another
  As illustrated in Figure 1–13,
    binary data are transferred in two ways: serial and parallel.
  Serial
    sent one bit at a time along a single line During the time interval from t0 to t1, the first bit is transferred.
    During the time interval from t1 to t2, the second bit is transferred, and so on.
    To transfer eight bits in series, it takes eight time-intervals.

## Slide 47: A Digital Waveform Carries Binary Information
Data Transfer
  parallel
    When bits are transferred in parallel form, all the bits in a group are sent out on separate lines at the same time.
    There is one line for each bit as shown in Figure 1–13(b)
    To transfer eight bits in parallel, it takes one time interval compared to eight time intervals for the serial transfer.
  an advantage
    of serial transfer of binary data is that a minimum of only one line is required.
    In parallel transfer, a number of lines equal to the number of bits to be transferred at one time is required.
  A disadvantage
    of serial transfer is that it takes longer to transfer a given number of bits than with parallel transfer at the same clock frequency
    parallel transfer takes more lines than serial transfer.

## Slide 48: A Digital Waveform Carries Binary Information
Data Transfer

## Slide 49: A Digital Waveform Carries Binary Information

## Slide 50: A Digital Waveform Carries Binary Information

## Slide 51: 1–3 Basic Logic Functions
logic is the realm of human reasoning
  that tells you a certain proposition (declarative statement)
    is true if certain conditions are true.
  Propositions can be classified as true or false.
    Yes or no
  Several propositions, when combined
    form propositional, or logic, functions.
    For example, the propositional statement
      “The light is on” will be true if “The bulb is not burned out” is true and if “The switch is on” is true.
      Therefore, this logical statement can be made: The light is on only if the bulb is not burned out and the switch is on.
      In this example the first statement is true only if the last two statements are true.
        The first statement (“The light is on”) is then the basic proposition
        the other two statements are the conditions on which the proposition depends.